## Slide 1: The Components of a Computer System- Recap
1
Von Neumann architecture is based on the following three characteristics
  Four major subsystems called
    memory
    input/output
    arithmetic/logic unit (ALU)
    control unit
  The stored program concept
  The sequential execution of instructions

## Slide 2
Components of the Von Neumann Architecture

## Slide 3: Machine Language Instructions
Instructions that can be decoded and executed by the control unit of a computer
Operation code field
  Unique unsigned integer code assigned to each machine language operation recognized by the hardware
Address field(s)
  Memory addresses of values on which the operation will work

## Slide 4
Typical Machine Language Instruction Format

## Slide 5: Machine Language Instructions (continued)
Instruction set
  Set of all operations that can be executed by a processor
Reduced instruction set computers or RISC machines
  Include as little as 30–50 instructions
Complex instruction set computers (CISC machines)
  Include 300–500 very powerful instructions

## Slide 6: Machine Language Instructions (continued)
Classes of machine language instructions
  Data transfer
  Arithmetic
  Compare
  Branch

## Slide 7: Control Unit Registers and Circuits
Program counter (PC)
  Holds the address of the next instruction to be executed
Instruction register (IR)
  Holds a copy of the instruction fetched from memory
Instruction decoder
  Determines what instruction is in the IR

## Slide 8
Examples of Simple Machine Language Instruction Sequences

## Slide 9
The Instruction Decoder

## Slide 10
The Organization of a Von Neumann Computer

## Slide 11
Instruction Set for a Von Neumann Machine

## Slide 12: LAB
Motherboard Theatre of LMC
  Littleman Simulator
handout of Instruction set

## Slide 13: Non-Von Neumann Architectures
Problems that computers are being asked to solve
  Have grown significantly in size and complexity
Important limit on increased processor speed
  Inability to place gates close together on a chip
Slowing down
  Rate of increase in performance of newer machines
Von Neumann bottleneck
  Inability of the sequential one-instruction-at-a-time Von Neumann model to handle today’s large-scale problems

## Slide 14: Non-Von Neumann Architectures (continued)
Parallel processing
  Building computers not with one processor, but with tens, hundreds, or even thousands
SIMD parallel processing
  ALU is replicated many times
  Each ALU has its own local memory where it may keep private data
MIMD parallel processing
  All processors are replicated
  Every processor is capable of executing its own separate program

## Slide 15
A Parallel Processing System

## Slide 16: Non-Von Neumann Architectures (continued)
Scalability
  It is possible to match the number of processors to the size of the problem
Massively parallel MIMD machines
  Have achieved solutions to large problems thousands of times faster than is possible using a single processor
Grid computing
  Enables researchers to easily and transparently access computer facilities without regard for their location